## Slide 1: Windmill Farm Optimization Using Genetic Algorithms
Marjon Santiago

## Slide 2: Table of Contents: 1. Problem 2. Rationale/Background 3. Possible Solutions 4. My Solution/Simulation 5. Closing Statement 6. Works Cited

## Slide 3: Problem
Main push: A global need to invest more into renewable energy sources
The main reason against using Wind Turbines is the cost to performance output
Wind Turbines are expensive to install and produce, but cheap to maintain
Proper care needs to be made when placing them together in Wind Farms to maximize their performance and energy output in the long run, while reducing cost of implementation
https://www.ge.com/reports/size-matters-next-big-thing-wind-turbines/

## Slide 4: Rationale
A heavy need to turn to renewable resources—relying on nonrenewable resources such as coal, oil, and natural gas for electricity is unsustainable for the environment.
Wind farms can last for a very long time without much maintenance and is therefore a long-term solution
The cost barrier is the number one thing preventing investment (the output of energy to the cost of development). The solution is to reduce the cost of production or to improve the output energy of wind farms, or both.

## Slide 5: Possible Solution: Genetic Algorithm 1

## Slide 6: Possible Solution: Genetic Algorithm 1
Quick explanation of a basic Genetic Algorithm:
  The problem with optimizing Wind Farms is that there are too many possible arrangements to find the solution with brute force
  Genetic Algorithm is designed to start with a randomized data set and tries to approach a solution by selectively choosing more and more fit members of a data set
Keywords to Remember:
  Fitness: a score assigned to a member of the data set that determines the probability of passing genes to the next generation
  Mutation: introducing variety into a population/data set by randomizing a specific part of a member’s gene or data.
  Substation: a center or a group of centers that collect the electricity generated by the wind turbines.
https://en.wikipedia.org/wiki/Darwin%27s_finches
https://towardsdatascience.com/introduction-to-evolutionary-algorithms-a8594b484ac

## Slide 7: Possible Solution: Genetic Algorithm 1
The solution provided by given research looks at a few factors[1]:
  The voltage level inside the wind farm
  The voltage levels of substation
  The number of substations
  The connection topology of substations
  The connections topologies of turbines
All of these factors contribute to the cost of the electric system of the wind farm—let’s denote that with Ecost. The problem can be reduced to finding a layout that minimizes Ecost.
This algorithm is primarily concerned with offshore wind farms, we’ll cover a land wind farm in the next Genetic Algorithm solution.
[1]: Optimization of Electrical Connection Scheme for Large Offshore Wind Farm with Genetic Algorithm, page 1, 05348118

## Slide 8: Possible Solution: Genetic Algorithm 1
Constraints:
  Sbranch <= Smax
  Sbranch is the amount of power a generated configuration transmits
  Smax is the maximum “real life” power that each configuration is rated to support
Any configuration that does not follow this constraint cannot be the final solution.

## Slide 9: Possible Solution: Genetic Algorithm 1
A few cost calculations need to be kept track of:
  Cost of transformers connected to wind turbines C1 = p1 * N
    P1 is the price of the transformer, N is the number of wind turbines
  Cost of substations C2i = (bhi * nhi) + (bli * nli) + (p2i * mi) + Ei + Si
    bhi and bli are the prices of the bays of high voltage and medium voltage, determined by the voltage levels of the substation. nhi and nli are the number of bays, p2i is the price of the transformer based on its capacity and voltage level, mi is the number of transformers in the substation, which usually turns out to be 2, Ei is the the cost of the station control equipment and miscellaneous things, and Si is the construction const for the substation.
  Cost of constructing a substation Si = p3(mi * k1 + nhi * k2 + nli * k3)
    K1 is the construction area of the transformer, k2 and k3 are the construction area of the high and low voltage bays, and p3 is the unit price of construction. mi is usually 2 (transformers)
  Cost of marine cables C3 = C31 + C32
    C31 and C32 are the costs of medium voltage cables and high voltage cables.
  C31 =
    n is the number of segments connecting two wind turbines, lj is the length of the j’th cable, and p4j is the price of the j’th cable. C32 is calculate in the same way.

## Slide 10: Possible Solution: Genetic Algorithm 1
The algorithm can be visualized with the following flowchart.
The “fitness” value of each randomly generated topology can finally be determined by:
  Ecost = C1 + C2 + C3
  Fitness F =
  In short, the lower the cost is, the higher the fitness value and therefore, the higher chance of reproduction.

## Slide 11: Possible Solution: Genetic Algorithm 1
Case Study: 580 wind turbines
Here is an example of a generated wind farm network.
You can notice some features of the network: large hexagonal regions concentrated around various substations

## Slide 12: Possible Solution: Genetic Algorithm 2

## Slide 13: Possible Solution: Genetic Algorithm 2
Similar to the first research, this solution will use a Genetic Algorithm, but will account for different factors.
Rather than a heavy emphasis on minimizing the cost of implementing the components of the wind farm, this solution focuses on maximizing the total amount of energy harvested by the wind farm.[2]
Uses the “Wake model”, which will be explained shortly.
Wind Farm Layout Optimization using Real Coded Multi-population Genetic Algorithm, 08723810, page 1

## Slide 14: Possible Solution: Genetic Algorithm 2
Wind Turbine Wake Model: In short, it is used to describe the flow of wind behind a turbine after it has harvested kinetic energy.
Relevant to a topic in Operating Systems: Shared System Resources.
  Wind Turbines are like processes and the wind is a shared resource, but unlike operating systems multiple turbines must access the shared resource at the same time.
  Deadlocks do not exist here.

## Slide 15: Possible Solution: Genetic Algorithm 2
Wind speed is calculated by the formula on the right.
uij = wind speed after the turbine
u0 = wind speed before the turbine
xij = distance between turbines
ri = radius of the second turbine caught in the downstream of the first turbine’s wind.
α = entrainment constant, which depends on the terrain
a = axial induction factor, or how much the velocity of the wind changes after the first turbine.

## Slide 16: Possible Solution: Genetic Algorithm 2
A few other notable formulas to use first:
Z = roughness of the terrain
Z0 = the height of the turbine.
Relating the inner radiuses of the affected turbines (ri and rj) to a.
CT = thrust coefficient
Relating final wind speed i to the initial wind speed 0, given a set of other windspeeds ij for j = 1 to N, minus i.
Betz’ Relation

## Slide 17: Possible Solution: Genetic Algorithm 2
Finally, to get the efficiency of a particular wind farm configuration, we need the power generated from the wind turbine, given the wind speed calculations.
η is efficiency of the wind turbine (which is highly dependent on real world implementations
ρ is the air’s density
A is the area of the wind turbine’s rotor
u is the wind speed as it hits the turbine.

## Slide 18: Possible Solution: Genetic Algorithm 2
To get our “fitness value”, we will divide the cost of creating that wind farm with a simple a equation where N is the number of wind turbines, and the “Objective” will be to minimize the cost to power generated ratio.

## Slide 19: Possible Solution Genetic Algorithm 2
Two case studies were simulated: A wind farm with 26 turbines (N=26), and a wind farm with 30 turbines (N=30). They each are tested in an area of 2000m x 2000m.
Each triangle represents one turbine.
Their resulting data was compared with other proposed algorithms for placing wind turbines,
  In both cases, this algorithm yields impressive results

## Slide 20: Evaluation of Solutions
Both solutions have several pros and several cons, focusing on different things to achieve the same result, and come up with entirely different simulation outcomes.
In order to compare them fairly, their strengths and weaknesses should be evaluated separately first.

## Slide 21
Pros | Cons
- Considers the cost of implementation at an extremely detailed level | - Is not terrain dependent since cost of placement is adaptable and does not fluctuate with terrain
- Hypothetical models/simulations are likely close to real life accuracy due to less chaotic variables | - Does not account for the efficiency of energy harvesting
Algorithm 1
Pros | Cons
- Accurate formulas for calculating the effects of wind turbines on wind speed | - Simulation ran on the assumption that wind patterns were not chaotic
- The algorithm takes into account many, many aspects of wind conversion | - The cost breakdown simplified to the number of turbines, though more costs are involved than just that
Algorithm 2

## Slide 22: Which one wins?
In my opinion, I believe Algorithm 2 wins because:
  It can factor in the cost formula given by Algorithm 1 very easily.
  Maximizing the amount of wind energy harvested is more important than minimizing the initial cost of placing the wind turbines.
    This is because wind turbines are extremely low-maintenance and can last for a very long time, so no matter what the initial cost is, the wind farm should eventually pay for itself.
The clustering of the wind farms in Algorithm 1 are slightly dubious because they minimize the cost of placement but might have unintended consequences with actually gathering wind energy. Those metrics need to be recorded.

## Slide 23: My Contribution: Genetic Algorithm 3
My goal is the following:
  Compromise between cost and performance by factoring in their fitness values separately
  Make the algorithms more realistic by introducing variable wind speeds in the middle of the simulation
  Testing conditions in which the turbines are placed in specific patterns such as grids or circles to find patterns

## Slide 24: My Contribution: Genetic Algorithm 3
The implementation will be in Java using the Swing library for GUI.
It will have a few features such as changing how a wind farm is generated based on positions
5 Classes that handle in order:
  Logic for the genetic algorithm
  Contents of an individual turbine
  Contents of an entire Wind Farm
  Handles the GUI
  Main Class, runs everything

## Slide 25: My Contribution: Genetic Algorithm 3
This is what the GUI looks like so far.

## Slide 26: My Contribution Genetic Algorithm 3
  This is what my Genetic Algorithm template looks like so far:
  generateWindFarm – contains the template for the algorithm. Calls the other methods.
  calculateFitness – updates the fitness values of our given population.
  generateBreedingPool – creates a breeding pool based on fitness values—those with higher fitness values are represented more.
  generateChildren – creates a new generation of by going through the Breeding Pool and selecting parents.
  createMutations – creates mutations in the Wind Farms to generate diversity in the “gene” pool.

## Slide 27: My Contribution: Genetic Algorithm 3
Left to do:
  Implement the equations given by the research papers
  Make the GUI interactive with event listeners

## Slide 28: Closing Statement
This research project has been really fun, and I hope you’ve enjoyed my presentation!

## Slide 29: Works Cited
H. Lingling, F. Yang and G. Xiaoming, "Optimization of electrical connection scheme for large offshore wind farm with genetic algorithm," 2009 International Conference on Sustainable Power Generation and Supply, Nanjing, 2009, http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=5348118&isnumber=534 7868
H. Lingling, F. Yang and G. Xiaoming, "Optimization of electrical connection scheme for large offshore wind farm with genetic algorithm," 2009 International Conference on Sustainable Power Generation and Supply, Nanjing, 2009, http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=5348118&isnumber=534 7868
"Genetic algorithm." Wikipedia, The Free Encyclopedia. 19 Aug 2019, https://simple.wikipedia.org/w/index.php?title=Genetic_algorithm&oldid=6640615